| Project Information |
| --- |
| "Organization of Production Shop on Plastic Wastes Processing on the Premises of ООО "Potok-К" |
| Name of Organization | Limited Liability Partnership "Potok-К" |
| Name of Project | Organization of Production Shop on Plastic Wastes Processing on the Premises of ООО "Potok-К” |
| Branch | Processing of plastic materials |
| Location | Pionerbaza, 2, urban village Kamskie Polyany |
| Project Description | The project stipulates implementation of the following measures: - basic repair of production shop; - purchase of technological equipment; - performance of certification works; - working capital financing. |
| Technology Description | During industrial entry of reworked plastics, they go through processing, which includes four steps. The first step is intended for cleaning, the second one is for washing, the third one is for water removal, and the forth and fifth ones are for drying. After drying, prepared materials fall on grinding. After that, crushed material falls on press funnel, where it is gripped by screw. By moving along the cylinder, the material is getting warm and is breaking down. Further the material is pressed through strand end in appropriate line tracer, where it is cooled and cut into granulates |
| Competitive Advantages of Technology | As initial feedstock there are served polymer wastes, upon that, end product is also feedstock, which is in great demand. Reworking of polymer is carried out almost on the same terms (and roughly with the same end-use properties), as initial plastics, which were the base for it. In addition, using 1 ton of secondary raw material economizes up to 0,7 tons of initial feedstock. |
| Product Description | The product of plastic materials’ processing is secondary granulate |
| Market Description | Market of secondary granulate is dynamically developing, furthermore, growing demand is too fast for the proposal to follow, what is connected with the absence of accurate assembly norms and utilization of polymeric wastes |
| Main Buyers | Main consumers of these goods are the enterprises, dealing with production of plastic items, polyethylene, and other polymers. |
| Competitors in the RT Market | In the RT market, there are represented up to 7 small companies, for which reworking of raw material is side activity. The limits between competitors are washing out by the reason of that not a single company cannot offer any definite price range and заранее guarantee product quality beforehand – all depends on the quality of initial feedstock and the time for its sorting and primary processing |
| Stage of Project Development | There has been worked out the business plan and bought necessary technological equipment. Production has been launched. |
| Contact Information |
| Gainutdinov Ilgiz Akhmetzakievich | Tel.: +7 (843) 570-40-16 |
| Deputy Director | Fax: +7 (843) 570-40-00 |
| State Non-Commercial Organization |  |
| “Investment and Venture Fund of the Republic of Tatarstan” |  |
| Name of Organization |  |
| Ипатов Александр Геннадьевич | Tel.: +7 (843) 224-54-00 |  |
| директор |  |  |
| ООО "Поток-К" |  |  |